## Slide 1: Automated Defect Detection and Visual Inspection
for Quality Control in Manufacturing
Detection
Manufacturing
Automation
Neural Networks
Name:
Mansi Sapariya
Registration Number:
2448036
Project:
NNDL ESE1 Project

## Slide 2: Introduction
The Problem with Manual Inspection
Our Solution
Manual Process
AI-Powered
Improved Efficiency
Traditional visual inspection methods are slow and inconsistent
Highly prone to human error
Leads to missed defects in manufacturing
Results in production delays and increased costs
Difficult to scale with increasing production volume
Automated visual defect detection system using advanced deep learning models
Fast, accurate, and scalable quality control
Reduces reliance on manual labor
Improves overall product quality
Enables real-time detection and quality assurance

## Slide 3: Problem Statement
Key Challenges in Manufacturing Quality Control
Limited Access to Technology
Many manufacturing environments, especially Small-to-Medium Enterprises (SMEs), lack access to scalable, automated quality control solutions
Detection Complexity
Creating robust systems that can not only identify and classify a wide range of defects but also localize them precisely remains a significant challenge
Workflow Integration
Need for deep learning-powered systems that can optimize quality control processes and seamlessly integrate into existing production workflows
Our Project Focus
This project addresses these challenges by developing a comprehensive deep learning-based visual inspection framework that is both accurate and accessible to manufacturers of all sizes. The system aims to optimize quality control processes, reduce defect rates, and improve overall production efficiency.

## Slide 4: Project Objectives
Develop a Deep Learning System
To create an automated visual defect detection system using deep learning techniques capable of accurately identifying and classifying defective vs. non-defective items.
1
Comprehensive Data Analysis
To perform a thorough Exploratory Data Analysis (EDA) on the MVTec Anomaly Detection dataset, evaluating image quality, understanding image properties, and comparing feature distributions between normal and defective samples.
2
Visualize and Analyze Defect Patterns
To analyze and visualize defect patterns and frequencies using class-wise heatmaps, histograms, and anomaly overlays to understand and predict common defect locations.
3
Implement and Evaluate Models
To implement and evaluate a set of complementary deep learning models (CAE, U-Net, and PatchCore) to ensure robust and reliable defect detection.
4
Pave the Way for Real-Time Integration
To create a foundation for integrating the inspection system into production lines, generating actionable insights for improving quality control workflows and optimizing resource allocation.
5
4
Neural Networks and Deep Learning Project Presentation

## Slide 5: Dataset Overview - MVTec AD
MVTec Anomaly Detection Dataset
Categories & Defect Types
Capsule
Circuit
Hazelnut
Toothbrush
Leather
Tile
Wood
Object Categories:
Bottle Cable Metal Nut Screw
Texture Categories:
Carpet Grid
Fabric Wallpaper
5,354
Total Images
3,629
Normal Training Images
1,725
Defective Test Images
73
Defect Variations
Why we chose this dataset:
Realistic industrial use case that supports both classification and segmentation, making it ideal for training robust models.
High-quality industrial benchmark dataset with over 5,000 high- resolution images
Contains 15 different object and texture categories
5
Neural Networks and Deep Learning Project Presentation
Each category includes normal training images and test images with various defects
Designed specifically for anomaly detection in industrial inspection scenarios
Realistic use case that supports both classification and segmentation tasks

## Slide 6: Methodology
Project Workflow
1 Data Preprocessing
Images were resized to uniform dimensions Normalized pixel values to range [0,1]
Applied data augmentation (rotation, flipping, brightness adjustments)
Exploratory Data Analysis (EDA)
2
Visualized class distributions between normal and defective samples Created defect frequency analysis
Generated heatmaps to identify common defect locations
3
Model Building
Convolutional Autoencoder (CAE): For reconstruction-based anomaly detection
U-Net: For pixel-level segmentation and defect localization PatchCore: For detecting subtle, feature-level anomalies
Interactive UI Development
4
Built Gradio web interface for interactive visualization Enabled real-time anomaly detection results Integrated side-by-side model comparison features
5 Evaluation Metrics
Mean Squared Error (MSE) for CAE reconstruction quality Mean Anomaly Mask for U-Net segmentation accuracy Anomaly Scores for PatchCore feature deviation detection
66
Neural Networks and Deep Learning Project Presentation

## Slide 7: Exploratory Data Analysis (EDA)
Data Integrity Check
100% Data Integrity Maintained
Class Distribution
Defect Visualization
Normal
Defective
Heatmap
Average Defect Heatmap Analysis
Heatmaps revealed that defects tend to cluster in specific structural areas (e.g., the rim of a bottle), providing insights for targeted inspections.
Low
Medium
High
6,452 images verified
All images valid and free of corruption
7
Neural Networks and Deep Learning Project Presentation
High-resolution images suitable for detailed analysis
Significant class imbalance detected
Majority of samples are normal (non- defective)
Used weighted sampling to prevent model bias
Side-by-side comparisons of normal vs. defective
Ground-truth mask overlays for precise localization
Heatmaps reveal defect clustering patterns

## Slide 8: Final Model Output Visualization
Gradio UI Visualization Interface
Original Image
Input test image from MVTec dataset
CAE Result
MSE Score:
0.0167
U-Net Result
Mean Mask:
0.4168
PatchCore Result
Anomaly Score:
0.4649
Interpretation of Model Outputs
CAE MSE Score
U-Net Mean Mask
Low score (e.g., 0.0167) indicates image is close to normal patterns
High score flags a global anomaly
Focuses on reconstruction-based detection
High value (e.g., 0.4168) suggests a large defect region
Precise pixel-level segmentation of defects
Highlights exact boundaries of anomalies
PatchCore Score
Medium-high score (e.g., 0.4649) indicates subtle feature-level deviation
Compares features to normal memory bank Effective for detecting small, nuanced defects
8
Neural Networks and Deep Learning Project Presentation

## Slide 9: Model Architectures
Convolutional Autoencoder
Input Image
Encoder
Latent Space
Decoder
U-Net Segmentation
Input Image
Output Mask
PatchCore
Input Image
ResNet Backbone
Memory Bank Feature Patches
Anomaly Score Map
Unsupervised encoder-decoder structure
Detects anomalies by measuring reconstruction error
High MSE indicates defects/anomalies
Multi-Model Approach: Complementary strengths for comprehensive defect detection
Global Anomalies Pixel-level Localization Subtle Feature Anomalies CAE U-Net PatchCore
Encoder-decoder with skip connections
Precise pixel-level defect localization
Outputs detailed segmentation masks
Feature-based anomaly detection
Compares test features to memory bank
Detects subtle, feature-level anomalies

## Slide 10: Model Justification
Multi-Model Approach Advantages
Our multi-model approach was designed to leverage the unique strengths of each architecture, creating a comprehensive and robust defect detection system that outperforms single-model solutions.
Convolutional Autoencoder (CAE)
Excels at identifying global anomalies by flagging deviations from the overall learned "normal" image pattern.
Global Pattern Recognition
Reconstruction-Based
U-Net Segmentation
Specializes in precise localization, generating pixel-wise segmentation masks that highlight the exact boundaries of a defect.
Precise Localization
Boundary Segmentation
PatchCore
Captures subtle, feature-level anomalies by comparing image patches to a memory bank of normal features, detecting small, nuanced defects.
Feature-Level Detection
Subtle Anomalies
Combined System Benefits
Input Image
CAE
U-Net
PatchCore
Parallel Processing
Robust Detection
Higher Accuracy
Fewer False Negatives
Diverse Defect Coverage
10
Neural Networks and Deep Learning Project Presentation

## Slide 11: Model Performance & Results
CAE Model
Mean Squared Error (MSE):
0.0167 (Normal Images)
0.1458 (Defective Images)
U-Net Model
Mean Anomaly Mask:
0.4168 (Defect Regions)
0.0213 (Normal Regions)
PatchCore Model
Anomaly Score:
0.4649 (Feature Deviation)
0.0128 (Normal Features)
Complementary Performance Across Defect Types
Key Finding: Combined multi-model approach provides more comprehensive and reliable detection than any single model, capturing different types of defects with high accuracy.
Successfully learned normal patterns Strong at detecting global anomalies Lower MSE indicates better image reconstruction
11
Neural Networks and Deep Learning Project Presentation
Precise pixel-level localization
High sensitivity to defect boundaries Higher mask values for pronounced defects
Best at subtle, feature-level anomalies Highest sensitivity to small defects Effective on spatially limited anomalies

## Slide 12: Conclusion
Project Achievements
We successfully developed a multi-model deep learning framework for automated visual defect detection using a real-world industrial dataset (MVTec AD). Our combined approach using CAE, U-Net, and PatchCore provides a more comprehensive and reliable solution than any single-model system alone.
Multi-Model Synergy
Combined strengths of three deep learning models to maximize detection capabilities across different defect types
Industrial Application
Scalable, accurate visual inspection system that reduces manual errors and optimizes production workflows
Quality Improvement
Enhanced product quality and reduced inspection costs through automated, consistent detection systems
Impact on Manufacturing Sector
Reduced manual inspection time
Enhanced defect localization
Improved production quality
Reduced operational costs

## Slide 13: Limitations & Future Scope
Current Limitations
Future Opportunities
Current Challenges
Ongoing Research
Future Applications
May not generalize well to entirely new defect types or component shapes
Requires additional training data for novel defect categories
Does not account for real-world variables such as lighting changes or motion blur
Computational requirements may be high for real-time applications
Deployment challenges in resource-constrained manufacturing environments
Integration with real-time video feeds for live production line monitoring
Deployment on edge devices for faster, on-site inference
Extension to multi-class defect classification
Advanced transfer learning techniques to adapt to new products with minimal retraining
Integration with robotic systems for automated quality control and sorting